## Slide 1
Multi-Phase CT Registration Pipeline
Data Science & Machine Learning Lab
Sharif University of Technology
Summer 2025

## Slide 2
Outline
1. Motivation
2. Dataset Overview
3. Registration Pipeline
4. Z-Alignment Method
5. Rigid Registration
6. Deformable Registration
7. Evaluation Metrics
8. Future Work

## Slide 3
Motivation

## Slide 4
Motivation
Goal: Generate Contrast-Enhanced CT (CECT) from Non-Contrast CT (NCCT)
●
Non-contrast CTs are hard to directly segment — contrast helps
●
Contrast phases are not always available due to clinical or cost constraints
●
Deep learning models trained on NCCT→CECT require well-aligned multi-phase pairs
Problem found in practice:
➤
Publicly available multi-phase CT datasets have unregistered, misaligned phases
➤
Phases acquired at different table positions — Z-coverage does not match
➤
Large HU intensity differences between phases (NCCT ≠ CECT)
➤
Standard registration metrics (MMI, NCC) are not valid across contrast phases

## Slide 5
Dataset Overview

## Slide 6
Dataset
➤
VinDr multi-phase abdominal CT dataset — phase labels provided per study
3
Phases per study
NC · Arterial · Venous
~265
Studies
Two scanner sessions
1.5 mm
Isotropic target
After resampling
Vindr_ds characteristics:
-
Phase DICOMs provided with phase labels per SeriesInstanceUID
-
Covered phases: non-contrast, arterial, venous
-
Two different scanner models → different HU baselines across studies
-
Standardized to LPS orientation and isotropic 1.5 mm spacing

## Slide 7
Registration Pipeline

## Slide 8
Registration Pipeline
LPS orientation
1.5mm isotropic
HU clip [−1024,+1024]
DICOM
→ NIfTI
1
TotalSegmentator
seg_full + seg_reg
dual mask output
Segmentation
2
3D organ centroid
MAD outlier filter
confidence gate
Z-Alignment
(v3)
3
Kabsch SVD init
Dice+centroid loss
MMI polish
Rigid
Registration
4
B-spline MMI
25mm grid spacing
organ mask constrained
Deformable
Registration
5
Evaluation: Eroded Dice + Centroid Displacement (mm) per organ, per phase, per stage

## Slide 9
Z-Alignment Method

## Slide 10
Z-Alignment (v3)
3D centroid
alignment
physical mm
space
confidence
gated
Why Z-Alignment is needed:
➤
Different phases are acquired at different table positions → Z-coverage does not match
➤
Must find a common overlapping Z-window before any registration
Algorithm (3D centroid matching):
1
Compute weighted 3D physical centroid of anchor organs (liver w=3, spleen w=2, kidneys w=2) independently in NC and each moving phase
2
MAD outlier filter removes rogue organ centroids (unweighted median, floor 5mm)
3
If confidence ≥ 0.40 and |offset| ≤ 80mm → use 3D centroid offset; else fall back to per-series Z-centre crop
4
Crop all series to the common Z-overlap window with forced matching physical origins

## Slide 11
Rigid Registration

## Slide 12
Rigid Registration
Pass 0a
Kabsch SVD
(Bone Only)
Closed-form centroid alignment on vertebrae, ribs, spinal cord. Weighted SVD — instant, no iteration. Provides initialization for Pass 0b.
Pass 0b
Kabsch SVD
(All Organs)
Extends Kabsch to all stable organs: liver, spleen, kidneys, aorta, IVC, muscles. Weighted by organ reliability. Initializes Pass 1.
Pass 1
Dice + Centroid
Refinement
Nelder-Mead minimizing Σ wᵢ [centroid_dist + λ·(1−Dice)] / Σwᵢ. All organ data precomputed once (~100× speedup vs naive).
Pass 2
MMI Polish
Mattes Mutual Information with organ mask. Currently gated — only applied when Pass 1 centroid error improves.

## Slide 13
Why Segmentation-Based Loss?
Intensity-
based metrics
fail across
contrast
phases
Use anatomy
instead
Standard metrics are not valid across NCCT ↔ CECT:
MMI
✗ Invalid
Assumes stable joint histogram — contrast timing changes the histogram relationship between NCCT and CECT
NCC
✗ Invalid
Assumes fixed linear intensity relationship — contrast enhancement breaks this (aorta: 40→300 HU while surrounding tissue unchanged)
Our approach: Segmentation-Based Loss
✓
Anatomy-based: segmentation masks are phase-agnostic — no HU assumptions
✓
Eroded Dice: measures shape overlap inside organs, independent of intensity
✓
Centroid distance: measures positional alignment in physical mm space

## Slide 14
Deformable Registration

## Slide 15
Deformable Registration
➤
B-spline deformable registration applied after rigid alignment
algorithms tested:
✓
Rigid
✓
Affine
✓
B-spline (25mm grid spacing, LBFGSB optimizer)
○
VoxelMorph (planned — future work)
Configuration:
-
Metric: Mattes Mutual Information (50 histogram bins)
-
Mask: NC seg_reg organ mask (fixed) + dilated mask (moving, 12mm extra)
-
Optimizer: LBFGSB · convergence tolerance 1e-5
-
Multi-resolution: [4,2,1] shrink factors, smoothing [2.0, 1.0, 0.0] mm

## Slide 16
Evaluation Metrics

## Slide 17
Evaluation Metrics
Phase-agnostic metrics — no HU assumptions, anatomy-based only
Eroded Dice Coefficient
2 · |erode(M_fixed) ∩ erode(M_moving)|
──────────────────────────────────────
|erode(M_fixed)| + |erode(M_moving)|
Erosion (6mm): removes boundary uncertainty from segmentation inaccuracies
Phase-agnostic: measures shape overlap using masks, not HU values
Scope: all stable organs in seg_reg
Centroid Displacement (mm)
‖ centroid_fixed − centroid_moving ‖₂ (mm)
Full 3D mask: averaging over the whole volume is robust to boundary noise
Clinical scale: < 5mm excellent · 5–10mm acceptable · > 15mm failure
Scope: all stable organs in seg_reg
NCC (Normalized Cross-Correlation) — EXCLUDED: assumes fixed linear intensity relationship between phases. Contrast enhancement breaks this — values become meaningless for NCCT ↔ CECT comparisons.

## Slide 18
Segmentation Mask Architecture
TotalSegmentator produces per-organ .nii.gz files → combined into two masks:
seg_full
All organs · bounding box
Tier 1: Bones (labels 21–99)
vertebrae, ribs, sternum, hips
Tier 2: Stable soft (labels 1–20)
liver, spleen, kidneys, vessels
Tier 3: Other soft (labels 100–149)
stomach, bladder, adrenals
GUT EXCLUDED entirely
(colon, bowel, rectum, duodenum)
Purpose: define abdominal crop box
seg_reg
Stable only · registration metric
Tier 1 + Tier 2 ONLY
Bones: vertebrae, ribs, sternum,
hips, femurs, sacrum
Soft: liver, spleen, kidneys,
aorta, IVC, muscles
Purpose: all registration
passes + evaluation
Labels are fixed integers
(not positional)
Gut excluded from both masks — too variable for registration (colon, small bowel, rectum, duodenum)

## Slide 19
Future Work

## Slide 20
Future Work
Applying the segmentation-based metric across registration algorithms:
✓
Rigid
Kabsch SVD + Dice+Centroid refinement — implemented and tested
✓
Affine
Extension of rigid with shear/scale — implemented
✓
B-spline
25mm grid, LBFGSB optimizer — implemented and tested
○
VoxelMorph
Finetune and evaluate using the same eroded Dice + centroid metric
Next steps:
➤
Run full pipeline on corrected VinDr cohort (crop → Z-align → rigid → deformable)
➤
Quantitative comparison: Dice + centroid per organ, per phase, per registration stage
➤
Ablation study: baseline crop only vs +rigid vs +deformable
➤
Return to original goal: NCCT → CECT generation with properly aligned training pairs

## Slide 21
Thank You!
Any Questions?